## Slide 1: Basis of frequency analysis Important concepts for EEG application
M-BIC: Disclosing fine-grained temporal processing: Common and advanced analysis of EEG time-series
Sanne ten Oever

## Slide 2
Outline:
Fourier analysis
  Basis
  Tapering
  Assumptions
Fourier for interpretation of EEG data
  Evoked power, induced power, ITC

## Slide 3: Fourier
One of the Fundamental Secrets of the Universe
"All waveforms, no matter what you scribble or observe in the universe, are actually just the sum of simple sinusoids of different frequencies"
Joseph Fourier (18th C.)

## Slide 4
EEG is sampled data (compared to continuous data), thus we work with discrete Fourier transforms
Which can be computed fast with fast fourier transforms (FFT)
  Most optimal at 2^n
Notes: https://jakevdp.github.io/blog/2013/08/28/understanding-the-fft/

## Slide 5: Basis of Fourier: explained via covariation of sine and cosine
Some data:
  100 Hz sample rate
  1 sec
  5 Hz
  Noise added
  Demeaned

## Slide 6: Matlab FFT

## Slide 7
= 0

## Slide 8: Matlab FFT

## Slide 9: Amount of points in freq axis
Notes: 600/120 = 5 cycle for it = 5.

## Slide 10: “aliasing” in the FFT

## Slide 11
All frequencies are captured in half of the spectrum
Still to transform to Hertz, now in data units, not time.
In other words:
  Amount of frequencies estimated: Nsamples/2+1
  Frequency resolution: 1/LengthTimeWindow

## Slide 12: Matlab FFT

## Slide 13
Notes: + 0.25 pi

## Slide 14: Get full spectrum

## Slide 15: Sin and cosine together make phase
vs
100% sin
50% sin
50% cos

## Slide 16: Complex Fourier spectrum
Real axis: cosine
Imaginary axis: sine
Eulers formula:
With amplitude:

## Slide 17
100 Hz sample rate
0.9 sec
5 Hz
Demeaned
In fieldtrip structure
Full story of toolbox FFTs?

## Slide 18: Fieldtrip FFT
Ask for method mtmfft: fft
Output power
Taper: later
pow = (amp).^2
amp = sqrt(pow)

## Slide 19: Matlab FFT
Function: fft
Normalized
Get amplitude.
  Function abs
Notes: Frobenius normalization = square root of the sum of the absolute squares of its elements
Code: A/sqrt(sum((A.^2))

## Slide 20: Fieldtrip output seems more narrow

## Slide 21: Spectral leakage
5 Hz
5.6 Hz

## Slide 22: Periodic assumption
5 Hz
5.6 Hz

## Slide 23: “Solution”: Tapering

## Slide 24
Before tapering
After tapering

## Slide 25: Different kinds of tapers

## Slide 26: Different kinds of tapers (dB)
Narrowing down + leakage at wider range

## Slide 27
Most EEG applications prefer leakage around the frequency of interest than wider band leakage
  Hanning

## Slide 28: Multi-tapering
Reduce noise by estimate power at different independent instances

## Slide 29
Notes: discrete prolate spheroidal sequence: max suppressed sidelobes (Hanning like).

## Slide 30: Multi-tapering
Notes: More tapers for higher smoothing. Exact taper amount then depends again on width of the time window (as that is related to the frequency resolution).

## Slide 32: Dpss vs Hanning
Note: dpss without smoothing (at frequency resolution, 1 taper) is equal to Hanning

## Slide 33
“All waveforms, no matter what you scribble or observe in the universe, are actually just the sum of simple sinusoids of different frequencies”
The world only consist of sinuses?
  No!
  Just another mathematical description of your data.

## Slide 34: Some non-sinus Fourier output
Hanning taper

## Slide 35: Some other sinus-like data
Hanning taper

## Slide 36: Some non-sinus Fourier output
no taper

## Slide 37: Some other sinus-like data
No taper

## Slide 38: Padding
Frequency resolution: 1/LengthTimeWindow
Why not just increase our time window by adding zeros!

## Slide 40: Padding

## Slide 42: To the other side: phase.
Power: abs(complexFourier).^2
Phase: angle(complexFourier)

## Slide 43: Circular data: point estimate, but need time integration
@ convention of matlab.
Notes: In other applications peak is 0.5pi

## Slide 45: Reliability of phase estimation

## Slide 46: Interpreting absolute EEG phase
Summation of many currents
Difficult to interpret it as depolarized/hyperpolarized
Might be consistent within a subject, but not over a subjects

## Slide 47
Important note:
  Normal FFT estimates phase for the whole window > so at the middle point
  Fieldtrip adjusts this FFT phase by the phase distance of data point 1 with time 0.
  Why? no idea.
Notes: determine phase-shift so that for all frequencies angle(t=0) = 0 (line 216 of ft_specest_mtmfft)

## Slide 48: What should you take from this when you do your EEG Fourier
Your frequency resolution depends on the window length you put in the FFT.
  You cannot distinguish theta from alpha with short window lengths (even with padding)
You cannot estimate high frequencies with a low sampling rate
  Gamma needs higher sampling rates
There will always be some spectral leakage
  Be cautious with interpreting nearby frequencies
Non-period signals also give a non-zero power spectrum.
  Not everything is an oscillation! Look at your spectrum and do not only extract specific bands.
Phase cannot be interpreted well at very low power
Is your signal really periodic at the frequency of interest?
  Time-frequency analysis

## Slide 49: More real data

## Slide 50
How to deal with this:
  Transform
    decibels
  Baseline
  Conditions
  Remove 1/f trend trough fitting
  Might be a signal though! (Voytek et al., 2015)

## Slide 51: Example: eyes open/eyes closed

## Slide 52: Most typical measures with EEG
Evoked power
Induced power
Inter-trial coherence

## Slide 53: Evoked power
Power of your ERP
Single FFT estimation per condition per participant.
Phase locked power only

## Slide 54: Evoked power - SSVEP
Keitel et al., 2017
Notes: Keitel, 2017;

## Slide 55: Induced power
Estimate power for individual trials
Average the power spectra
Phase and non-phase locked estimates

## Slide 56: Induced power: alpha power
Heagens et al., 2011
Notes: Heagens et al., 2011

## Slide 57: Inter-trial coherence
Phase consistency over trials
Careful with in interpreting when differences in induced power.
  Lower power, more noisy phase estimate > lower ITC
But could provide interesting additional information

## Slide 58: ITC – sensory entrainment
Ten Oever et al., 2017
Notes: Ten Oever et al., 2017

## Slide 60
Very useful to have a deeper understanding of what you are doing with your data
Be careful interpreting your effect
Unpredictable responses could occur
Always look at the full spectrum!
Always look at the raw data and ERPs

## Slide 61
Thank you for listening